## Slide 1: Availability of GAST D versus Ground Broadcast EIG Parameters and Airborne Geometry Screening
Matt Harris, Paul Schlais

## Slide 2: Simulation Assumptions

## Slide 3: Availability Simulation Assumptions (1/4)
VPL, LPL Equations
  σDV, σDL assumed to be 15% of σvert, and σlat in the position domain, used 2-σ value for DV, DL in availability
    Reference: Murphy, Harris, Beauchamp, “Implications of 30-Second Smoothing for GBAS Approach Service Type D”, ION ITM 2010
  GAST = D, M = 4, Kffmd = 5.847, h0 = 14300 m, sn = 25, Dh = 15.24 m, svert_iono_gradient_x = 4 mm/km, t = 30s, vair = 81 m/s,
  xair dependent on EIG, see next slide
spr_gnd for < 35
spr_gnd for ≥ 35,
(AAD B)
(GAD C)

## Slide 4: Availability Simulation Assumptions (2/4)
User Distance from GBAS (xair)
  Dependent on assumed EIG, linear:
  Assume YEIG = 0.2 m, MEIG = 0.5 m/km (500 mm/km)
Chart: xair , Distance GBAS to Threshold (km)
| 0 | 8
Y-Values | 0.2 | 4.2
EIG | 2.5 m | 2.75 m | 3.0 m | 3.25 m | 3.5 m
Xair | 4.6 km | 5.1 km | 5.6 km | 6.1 km | 6.6 km

## Slide 5: Availability Simulation Assumptions (3/4)
User Locations
  Grid-like pattern for half hemisphere (1/4 globe)
    Approx. equidistant spacing
    Contains all the unique data necessary to apply to full globe
  Half hemisphere results applied to rest of globe
    Side study on a simple full-world run confirmed only half hemisphere is necessary
    Mirrored over equator
    Translated 90° longitude
  One minute time steps
    sidereal day (1436 minutes)

## Slide 6: Availability Simulation Assumptions (4/4)
Constellation
  “Martinez” = 24-Slot Standard Constellation
  “Expanded 24” = 27-slot Standard Constellation
  “Current” Constellation – Week 42 YUMA (Expanded 24 with spares = 32 sats)
State Probabilitites
  “RTCA/Minimum” Constellation State Probabilities:
  “Historical” Constellation State Probabilities:
N = 24 | N = 23 | N = 22 | N = 21 | N < 21
95.0 % | 3.0 % | 1.2 % | 0.8 % | 0 %
N = 24 | N = 23 | N = 22 | N = 21 | N < 21
98.3 % | 0.6 % | 1.0 % | 0.1 % | 0 %

## Slide 7: Simulation Results

## Slide 8: Availability Results Maps Layout Constellation State = [24=X%, 23=X%, 22=X%, 21=X%, <21=X%]
Svert2 < 3.2
Svert2 < 2.91
Svert2 < 2.67
Svert2 < 2.46
Svert2 < 2.23
Svert2 < 4
Svert2 < 4.31
Svert2 < 4.67
Svert2 < 5.09
Svert2 < 5.6
Svert2 < 4
Svert2 < 4
Svert2 < 3.33
Svert2 < 3.43
Svert2 < 2.86
Svert2 < 2.86
Svert2 < 3.69
Svert2 < 4.36
Svert2 < 4.8
Svert2 < 3.63
EIG
EV
Svert2 < maxEv / EIG

## Slide 9: Availability of xPL < xAL Only (no Svert Limit) Martinez + RTCA / Minimum Constellation State = [24=95%, 23=3%, 22=1.2%, 21=0.8%, <21=0%]
Distance and VPL are not driving availability
Xair = 4.6 km | Xair = 5.1 km | Xair = 5.6 km | Xair = 6.1 km | Xair = 6.6 km

## Slide 10: Availability of XPL < XAL & Svert2 < EV / EIG Martinez + RTCA / Minimum Constellation State = [24=95%, 23=3%, 22=1.2%, 21=0.8%, <21=0%]
Xair = 4.6 km | Xair = 5.1 km | Xair = 5.6 km | Xair = 6.1 km | Xair = 6.6 km

## Slide 11: Availability of XPL < XAL & Svert2 < EV / EIG Martinez + Historical Constellation State = [24=98.3%, 23=0.6%, 22=1.0%, 21=0.1%, <21=0%]
Xair = 4.6 km | Xair = 5.1 km | Xair = 5.6 km | Xair = 6.1 km | Xair = 6.6 km

## Slide 12: Availability of XPL < XAL & Svert2 < EV / EIG Expanded 24 + RTCA / Minimum Constellation State = [27=95%, 26=3%, 25=1.2%, 24=0.8%, <21=0%]
Xair = 4.6 km | Xair = 5.1 km | Xair = 5.6 km | Xair = 6.1 km | Xair = 6.6 km

## Slide 13: Availability of XPL < XAL & Svert2 < EV / EIG Week 42 YUMA + RTCA / Minimum Constellation State = [31=95%, 30=3%, 29=1.2%, 28=0.8%, <28=0%]
Xair = 4.6 km | Xair = 5.1 km | Xair = 5.6 km | Xair = 6.1 km | Xair = 6.6 km

## Slide 14: Availability of XPL < XAL & Svert2 < EV / EIG Week 42 YUMA + Historical Constellation State = [31=98.3%, 30=0.6%, 29=1.0%, 28=0.1%, <28=0%]
Xair = 4.6 km | Xair = 5.1 km | Xair = 5.6 km | Xair = 6.1 km | Xair = 6.6 km
31